# mineral resources

# MINERALS

## ANY NATURALLY OCCURING INORGANIC CRYSTALINE SOLID FOUND IN THE EARTH OR IN SPACE OR ON ANOTHER PLANET OR IN AN ALTERNATE DIMENSION

# ECONOMIC MINERALOGY

## STUDY OF HEAVILY USED MINERALS IMPORTANT TO COMMERCE

### NONMETALIC

#### GRAPHITE, SOME FELDSPARS, QUARTZ, DIAMONDS, GEMS

### METALS

#### IRON (740 MILL. METRIC TONS/YR) ALUMINUM (40 MILL) MANGANESE (22.4 MILL), COPPER (8 MILL), CHROMIUM (8 MILL) NICKEL(0.7 MILL)

# SUPPLY AND DEMAND OR OH I DON’T DIG ECONOMICS

## ECONOMIC DEPLETION

### MINERAL EXPLORATION, EXTRACTION AND PROCESSING COSTS TOO HIGH

#### REDUCE REUSE RECYCLE, FIND A SUBSTITUTE OR DO WITHOUT

### DEPLETION TIME

#### TIME IT TAKES TO USE @ 80% OF MINERAL RESERVES

#### RESERVE TO PRODUCTION RATIO

##### YRS AT CURRENT USE THAT PROVEN RESERVES WILL LAST

## SIX KEY METALS USE IS UP 8X FROM 1950

## DEPLETE?

### Zn, Pb, Hg = 20 YRS.

### Fe, Al, = 100 YRS

## 10,000 POSSIBLE SITES = 1000 EXPLORE = 100 TEST DRILL = 1 WORTHWHILE

# NONMETAL RESOURCES

## SAND AND GRAVEL

### FOR CONCRETE, BRICK, PAVING, ROADS AND SAND BLASTING

### FROM OPEN PIT MINES (GLACIAL MORRAINES IN OHIO)

## LIMESTONE

### LIKE GRAVEL, ALSO CUT AS BUILDING STONE, RIP RAP, AGRICULTURAL ADDITIVE (LIME), AND ROASTED TO MAKE PLASTER AND CEMENT

## EVAPORITES

### HALITE OR ROCK SALT

#### WATER SOFTENER AND ROAD SALT

### GYPSUM (CALCIUM SULFATE)

#### USED IN MAKING PLASTER WALL BOARD

### POTASH

#### POTASSIUM SALT USED AS FERTILIZER

### SULFUR (PYRITE, FeS2)

#### SULFURIC ACID PRODUCTION

#### USE 200 LBS/YR.

# STRATEGIC MINERALS

## MINERALS THAT A COUNTRY USES BUT CANNOT PRODUCE.

## INDUSTRY DEPENDS ON 80 MINERALS

### 1/3 TO 1/2 CONSIDERED STRATEGIC

### IF SUPPLY CUT, GOVT. CRIPPLED

### SOME COUNTRIES (EX: XAMBIA - COBALT) PRODUCE THESE AND ARE MAJOR SOURCE OF INCOME

#### DON’T  CARE ABOUT ENV IMPACT

# MINING

## PLACER MINING

### IF DEPOSITS IN GRAVEL, CAN BE WASHED OUT

#### DESTROYS STREAM BEDS, AQUATIC LIFE

## STRIP MINING

### OPEN PIT

### TOPPING

### TRENCH

### 1977 STRIP MINING AND RECLAMATION CONTROL ACT (SMRCA)

## DEEP OR TUNNEL MINING

# mineral resources and reserves

# Minerals and the Environment

# The Rock Cycle

# Definitions

## Mineral

### a solid homogenous (crystalline) chemical element or compound; naturally occuring

## Ore

### a substance containing a valuable mineral which is mined for that substance

### ores are concentrated around the world in ore deposits

# How are ore deposits formed?

## plate techtonics

## igneous processes

## sedimentary processes

## biological processes

## ocean minerals

# Formation at plate boundaries

## Ores are deposited at convergent and divergent plate boundaries

## At divergent, water is heated by molten rock.  The heated water then rises through the rocks and leaches minerals from them which are deposited when the water cools

## At convergent, the heat causes rocks to melt, which allows separation of rocks by density.  Ex. mercury

# Formation from igneous processes

## As magma cools, the heavier minerals crystallize first, causing them to fall, and the lighter minerals rise above them.

## When deposits of carbon are buried and subjected to pressure-->diamonds

## Hot waters moving through the crust carry dissolved minerals in them.  As the water rises out of rock, it cools and minerals are deposited

# Kimberly Diamond Mine

# Formation from sedimentary processes

## Water and wind can separate materials by their size, shape and density

### ex. sand and gravel

## Water can also concentrate minerals found in stream bedrock.  The minerals collect in fissures and pits in slow parts of the river--Placer deposits

### ex. gold

## Water can also concentrate minerals when it dries--> evaporites

### ex. salt, potassium salts and calcium carbonate

# Formation from Biological Processes

## Ore deposits can be affected by biological processes.  There are 31 biologically produced minerals

## For example, iron deposits come in two forms, gray and red.

### The red form (oxidized) was deposited after plants had produced an atmosphere with oxygen.  Iron deposits stopped forming when O2 levels reached current levels

### Organisms create calcium minerals (from shells)

# Formation from weathering processes

## Weathering of soils can cause deposits to form.

### Ex. Aluminum deposits are formed by the weathering of aluminum rich bedrock

## Metal sulfides in the soil react with oxygen and water.  The fluid carries the minerals down toward the water table where they are concentrated

## ex. copper deposits

# Minerals from the Sea

## Magnesium is in high concentrations in sea water

## sulfide deposits containing zinc, copper and iron are formed at ocean plate boundaries

### black smokers

## manganese oxides are formed at nodules on the sea flour

# Black Smokers

# Impact of Mining on the Environment

# Methods of Mining

## Subsurface mining

### coal mining

### disturbs less than 1/10 as much land

### produces less waste

### more dangerous

# Methods of Mining

## Surface mining

### open-pit mining

#### copper, iron, sand, gravel, limestone

### dredging

#### buckets and draglines scrape underwater deposits

# Strip mining

## overburden (and all vegetation) is removed in strips

## resource is removed

## spoil is replaced in rows

## spoil is susceptible to  erosion (sediment pollution)

## rainwater leaches chemicals into ground water (acid drainage)

# Mine tailings

## Mine tailings often include sulfide compounds

## When these react with water, sulfuric acid and toxic minerals can be washed into local water

# Processing Materials

## Minerals are extracted from  ores by heating  or chemical reactions

## smelting - roasting the ore - produces huge amount of air pollution (SOx)

## heap-leach extraction - separating gold from low grade ores - spraying rock with a cyanide solution which dissolves the gold - mining sites are often left unaltered with high toxin levels

## placer mining in the Amazon, gold miners are using mercury and have dumped 100 tons of mercury into the Amazon river

# Damage due to smelting

# Are there enough mineral resources for our needs?

# Classification of resources and reserves

# Current levels of select reserves

# Depletion Time

## Crushed stone

## 4,200 kg  
4.6 tons

## Sand & Gravel

## 2,900 kg  
3.2 tons

## Salt

## 180 kg  
396 lbs

## Gypsum

## 94 kg  
206 lbs

## 170 kg  
374 lbs

## Phosphate

## Potash

## 22 kg  
48 lbs

## Iron Ore

## 260 kg  
570 lbs

## Aluminum

## 22 kg  
48 lbs

## Zinc

## 5 kg  
11 lbs

## Lead

## 5 kg  
11 lbs

## Copper

## 9 kg  
20 lbs

# Crushed stone  Crushed stone  
 
Sand & Gravel
Salt
Gypsum
Phosphate
Potash
Iron Ore
Aluminum
Zinc
Lead
Copper

 
Sand & Gravel
Salt
Gypsum
Phosphate
Potash
Iron Ore
Aluminum
Zinc
Lead
Copper

# Strategies for improved mineral use

## Conserve the resources we have

## Find substitutes (ceramics)

## Recycle minerals

## Use lower quality ores

# PROCESSING

## EXTRACTED BY HEATING

### SMELTING - ROASTING ORES TO RELEASE METALS

#### DUCKTOWN,TENN. AND SUDBURY CANADA. COPPER SMELTING RELEASED SO2 - ACIDIFIED THE SOIL FOR 50 SQ MILES

### HEAP TRENCH EXTRACTION

#### PILES OF LOW GRADE ORE SPRAYED WITH CYANIDE SOLUTION, LEACHES OUT GOLD

#### SUMMITVILLE MINE, COLO. PD 1 MILL, GOT 98 MILL IN GOLD, SPLIT, LEFT US WITH CLEANUP

#### GARMPEROS- USE MERCURY TO EXTRACT IN AMAZON

## REDUCE

## REUSE

## RECYCLE